SECTION 09642-Wood Gym Flooring

PART 1 – GENERAL

  - DESCRIPTION

- Related work specified under other sections.

- CONCRETE SUBFLOORS – SECTION 03___

- Subfloor depression for finished flooring is: 3/4” (existing)

  - QUALITY ASSURANCE

- Manufacturer

- Manufacturer of wood flooring shall be a firm specializing in manufacturing products specified in this section.

- Basis of design shall be provided by Horner Flooring Company, Dollar Bay, MI. Phone 906-482-1180, www.hornerflooring.com or equal approved prior to submission of bid.

- Materials other than those listed must be approved 10 days prior by written addendum.

Materials from non-approved manufacturers will not be accepted.

- Installer

- The installation of the floor system described in these specifications shall be completed by a firm familiar with the requirements of the system specified and fully experienced in procedures required for installing wood flooring manufactured by Horner Flooring.

- Installer shall be liable for all matters related to installation for a period of one year after the floor has been substantially installed and completed.

- Installer must have Horner installation accreditation and MFMA accreditation.

  - SUBMITTALS

- Specification - Submit Horner Flooring specification sheets and shop drawings as required.

- Sample - Submit required number of samples of the specified system as requested by the owner/architect.

- Maintenance Guidelines - Upon completion of floor, send the Horner Floor Maintenance Guide to the owner.  This guide will explain the proper HVAC and building maintenance requirements as well as floor cleaning and servicing guidelines to assure proper floor performance and longevity.

  - WORKING CONDITIONS

- The wood flooring and its components specified herein shall not be delivered or installed until all wet trades and overhead work is completed.  This includes all masonry, painting, plaster, tile, marble, and terrazzo, as well as all overhead mechanical trades.  The building shall be fully enclosed and weather tight and all permanent windows and doorways shall be installed.  Permanent heating and air conditioning shall be installed and working in accordance with building occupation requirements.

- The concrete substrate shall be determined fully cured by industry standards.  It shall be free of all foreign materials and broom cleaned when turned over to the floor installer.  Permanent HVAC units for the building shall have been operating a minimum of one week prior to the floor installation start up.

- During and after installation, building HVAC systems shall maintain a temperature and humidity range compatible with the expected high and low moisture content range of the flooring. The floor installer, based on the building’s HVAC control and geographical situation, shall determine this range.

- Flooring must be stored on site in a dry, well ventilated area while acclimating to site conditions. Moisture content of wood shall be consistent with the ambient conditions of the building as it will be maintained when occupied.

  - WARRANTY AND DISCLAIMER

- Horner Flooring, hereby warrants the materials it has supplied to be free from manufacturing defects for a period of one year.  This warranty is in lieu of and excludes all other warranties expressed or implied including any implied warranties of merchant ability or fitness for a particular purpose.

- During the warranty period, the floor shall not be recoated without the approval of the flooring contractor.

- The jobsite documentation forms by the flooring contractor shall become a part of the warranty and both the owner and flooring contractor shall retain record of said forms as a permanent reference for any abrogation.

- Flooring contractor warrants the install of the floor systems to be free from defects in materials and workmanship for a period of one year.

- Notification of claim shall be made within 30 days of discovery.

- It is the policy of Horner Flooring to continuously improve its line of products. Therefore, Horner Flooring reserves the right to change, modify, or discontinue systems, specifications and accessories of all products at any time without notice or obligation to purchaser.

PART 2 PRODUCTS

2.1. MATERIALS

- Subfloor –

- Pine S4S 1” X 6” to remain as existing

- Flooring –

- 25/32” x 2 1/4”,  1st grade, plain sawn, northern hard Maple flooring, TGEM, MFMA-RL grade marked and stamped as manufactured by Horner Flooring.

- Provide 1/64” expansion per board

- Base Bid pricing will include the installation of 25/32”, 2 ¼”,  1st grade Maple Flooring. Please provide alternate pricing to furnish and install 25/32”, 2 ¼”, 2nd and Better grade Maple Flooring.

- Fasteners –

- Flooring - 2” barbed cleats.

- Finish Materials – Bona Kemi

PART 3 - EXECUTION

3.1. PRE-INSTALLATION INSPECTION

- Room shall be broom cleaned and free of any foreign debris.

- Floor installer shall document site and working conditions prior to and during installation.  This documentation shall become a part of any warranty and may or may not affect fulfillment of any warranty.

3.2. INSTALLATION

- DEMO/DISPOSAL

- Carefully remove existing tongue and groove northern hardwood maple flooring and any felt paper off from existing sub-floor to remain.  Take precaution to not damage the existing 1” x 6” sub-floor and/or loosen masti cushion sleepers below.

- SUBFLOOR –

- Pull nails and prepare existing sub-floor for new northern hard maple flooring surface by re-stapling any loose sub-floor as needed for a sound sub-floor surface, and install new 15# felt paper.

- FLOORING -

- Install New tongue and groove Horner Maple flooring parallel with the long dimension of room.  Flooring shall be power nailed every 10” to 12” O.C. with all end joints properly driven tight.

- 1/64” expansion joints will be required between flooring strips throughout the floor.

  - FINISHING

- FLOOR SANDING

- Machine sand entire floor including both new maple with multiple grit papers to a smooth and uniform surface, free from edger marks and drum drops.

- Remove all sanding dust and lint from entire surface by vacuum and/or tack.

- FINISHING

- Inspect entire floor to be sure surface is ready to accept stain and finish.  Floor should be free from dust and debris.  Apply 2 coats of penetrating sanding sealer.

- Paint game lines as existing and apply no less than 2 coats of high gloss finish per our manufacturer’s instructions.

- Floor shall be buffed, cleaned and tacked between coats.

- Wall Base: Glue vented wall base on walls must be removed and cleaned

- Threshold: existing to remain

  - CLEANUP

- CLEANUP

- Remove excess debris and waste material from the work area.

- General Contractor shall lock floor area after floor is finished to allow proper curing time. If general contractor or owner requires use of gym before proper curing time, they shall protect the floor by covering with non-marring Kraft paper.

END OF SECTION 09642